## Slide 1: Natural isotope abundance correction
A new tool available to you via github:
https://github.com/BrynMarieR/natural_isotope_correction
Literature sources: Midani et al, 2016
Yang et al, 2009
Buescher et al, 2015

## Slide 2: Why do we need isotopic natural abundance (NA) correction?
Important to separate isotopic labelling that came from the addition of an isotopically labelled tracer and isotopic labelling that came from the natural abundance of stable isotopes.

## Slide 3: Use cases for NA correction
Quantitative measures of labelling substrate
  Mass isotopomer distribution analysis
  Metabolic flux analysis

## Slide 4: When do you not need NA correction?
Qualitative assessments of functional enrichment assays
  Especially in the case of small molecules (expected natural abundance is low)
Singly-labelled metabolites (simple subtraction-based method for correction is equivalent when just looking at the M+1 peak)

## Slide 5: Motivating example: Pyruvate
C3H3O3
Two in silico experiments: We want to know, what is the mass isotopomer distribution of the purposefully labelled portion?

## Slide 6: Two methods: “classical” and “skewed”
Classical method assumes that for any metabolite, the mass isotope distribution of an labeled standard (with known enrichment of isotopes) is equivalent to an unlabeled standard (without any enriched isotopes).
It is empirically known that this assumption is WRONG. Therefore, the “skewed” method was developed to take into account the change in isotope distributions due to experimental isotopic enrichment.

## Slide 7: A very simple implementation of the ”skewed” method for NA correction
Create input file of uncorrected, labelled peak intensities (normalized to parent peak = 1)
Run script
Output is a file with abundance of labelled species (normalized to parent peak = 1)

## Slide 8: Input file

## Slide 9: What’s happening inside the script?
MID = Mass isotopomer distribution
So, the observed MID is equal to the Correction Matrix (CM) of the molecule (in this case, pyruvate) times the corrected MID.
Then just solve for the corrected MID! Using non-negative least-squares solver to ensure that we get no negative peak values, as recommended by the literature and as present in IsoCor, which used to be used for isotope NA correction before the demise of pythonxy.

## Slide 10: Matrix Multiplication Step

## Slide 11: What’s happening inside the script?
MID = Mass isotopomer distribution
So, the observed MID is equal to the Correction Matrix (CM) of the molecule (in this case, pyruvate) times the corrected MID.
Then just solve for the corrected MID! Using non-negative least-squares solver to ensure that we get no negative peak values, as recommended by the literature and as present in IsoCor, which used to be used for isotope NA correction before the demise of pythonxy.

## Slide 12: Output file

## Slide 13: How much of a difference does it make to correct for NA of isotopologues?

## Slide 14: Numerical comparison of outputs
Input
Classical method
Skewed method

## Slide 15: How well does the skewed method work vs the classical method vs no correction?
In high-noise conditions, the error due to natural abundance (as compared to the noise error) is very small, and since the variance-weighted sum-of-squares-residual attempts to “correct” for the amount of error due to noise (variance), we see that all methods reach the goodness-of-fit cutoff.

## Slide 16: How much of a difference does this correction make in flux analysis?

## Slide 17: All details for running available on github
https://github.com/BrynMarieR/natural_isotope_correction

## Slide 18: Some notes
You will need to install R and a few R packages
Any elements in your compound which are not in the isotope_data file will need to be added to that file
The ideal would be to use unlabeled peaks to build correction matrices. Currently, correction matrices are generated analytically based on expected isotopomer distributions
Purity of the labelling reagent can be taken into account using a flag, e.g. `--purity 0.95`

## Slide 19: Conclusions
If you’re ONLY examining the M+1 peak, the classical and skewed approaches are the same if you only examine peak intensities (rather than normalizing to the parent peak)
If you are looking at M+2, M+3, M+4… peaks and doing NA correction, you should used the skewed method
Larger molecules lead to more heavy isotopologues “by chance”
More labels, more isotope distribution skew! Adding 5 labelled carbons will skew your experiment more than adding 2.
The actual percent change of peak intensities is fairly small, but can be critical in quantitative studies, e.g. metabolite flux analysis.